## Slide 1: River Sediment Parameterization (Literature Review)
Grain Size, Hyporheic Exchange, POM Settling

## Slide 2: Grain Size (d50) as the Master Variable
Core Equations:
  Porosity: Modeled as a function of the median grain size.
    (Boudreau, 1997)
  Kozeny-Carman Equation: Establishes the link between grain size and permeability ().
    (Bear, 1972; Carman, 1956)
Parameter Definitions:
  : Median Grain Size. Source: USGS NWIS or Field Sieving. Range: 0.1 – 1.0 mm (Fine to Coarse Sand).
  : Porosity. Source: Derived from or bulk density. Range: 0.30 - 0.45 .
Implementation Strategy:
  Current Code: Hardcoded (representative of mud/clay).
  Proposed: Use as a single site-level input to automate the initialization of and k.

## Slide 3: Hyporheic Zone Diffusion & Residence Time
Core Equations:
  Effective Diffusivity (): Molecular diffusion () enhanced by shear-driven advective pumping in sandy beds.
  Residence Time (): Determines the window for biogeochemical reactions; inversely proportional to permeability and flow .
  Key Insight: Higher k and lead to shorter but significantly higher total mass flux () .
Parameter Definitions:
  : tortuosity. : Shear Velocity. Source: Calculated from Slope () and Depth (): . Range: .
  : Longitudinal Dispersivity. Source: Literature value for river bedforms. Range: .
  : Molecular Diffusion. Source: Chemical constant. Typical Range: .
Implementation Strategy:
  Current Code: Fixed diffusion coefficient.
  Proposed: Update D as a function of (hydrodynamics) and (sedimentology).

## Slide 4: River POM Settling & Flocculation
Core Equations:
  Rouse Number (): Criteria for suspension vs. deposition.
  Threshold: If , organic matter is fully suspended; .
  Effective Deposition: Scouring occurs when bed shear stress () exceeds critical stress ().
  .
Parameter Definitions:
  : Characteristic Settling Velocity. Value: 0.34 mm/s (Lamb et al., 2020). : von Karman constant. Value: 0.41 (Dimensionless)
  : Bed Shear Stress. Source: Calculated as . Range: . : Critical Shear Stress. Source: Literature for organic flocs. Range: .
Implementation Strategy:
  Current Code: Fixed burial rate (v_sed).
  Proposed: Apply a "Scouring Switch" to the boundary flux; if (Suspension) or (Scouring), organic input .

## Slide 5: Reference
Grant, S. B. et al. Effective diffusivity and mass flux across the sediment-water interface in streams. Water Resour. Res. 48, W05548 (2012) .
Boano, F. et al. Hyporheic flow and transport processes: Mechanisms, models, and ecosystems. Rev. Geophys. 52, 603–679 (2014) .
Boudreau, B. P. Diagenetic Models and Their Implementation. (Springer, 1997) .
Lamb, M. P. et al. Mud in rivers transported as flocculated and suspended bed material. Nature Geosci. 13, 566–570 (2020).
Winterwerp, J. C. A simple model for turbulence-induced flocculation of cohesive sediment. J. Hydraul. Eng. 124, 430–436 (1998).
Cardenas, M. B., Wilson, J. L. & Zlotnik, V. A. Impact of river bedform-induced hyporheic flow on long-term residence time distributions. Water Resour. Res. 40, W08403 (2004) .
Bear, J. Dynamics of Fluids in Porous Media. (Dover Publications, 1972) .
Carman, P. C. Flow of Gases Through Porous Media. (Butterworths Scientific Publications, 1956) .

## Slide 6: Multiple Grain Size and Porosity Modeling
Core Equations:
  The Unified Packing Model predicts porosity dynamically based on volumetric fractions.
  (El-Husseiny, A., 2021)
Parameter Definitions:
  : Calculated porosity of the sediment mixture.
  : Porosity of the pure coarse gravel framework.
  : Porosity of the pure fine sediment.
  : Volumetric fraction of fine grains.
Implementation Strategy:
  Proposed: Define a threshold (e.g., 2 mm) to partition the sediment mixture, using the median grain size of each fraction to automate the initialization of baseline .

## Slide 7: Reference
El-Husseiny, A. Unified packing model for improved prediction of porosity and hydraulic conductivity of binary mixed soils. Water 13, 455 (2021).
Uchida, T., Kawahara, Y., Hayashi, Y. & Tateishi, A. Eulerian deposition model for sediment mixture in gravel-bed rivers with broad particle size distributions. J. Hydraul. Eng. 146, 04020071 (2020).
Bui, V. H., Bui, M. D. & Rutschmann, P. Advanced numerical modeling of sediment transport in gravel-bed rivers. Water 11, 550 (2019).

## Slide 8: Parameter change for river env
P = 1;
  previous 500; % pressure at depth [atm]
S = 0.1;
  previous 35; % salinity [ppt]
F_CaCO3 = 10;
  previous 2000; %100; %10;%500; % Flux of CaCO3 to sediment gram/m2/year
SO4init = 2000;
  previous 28000; % uM - SO4 concentration at SWI
k_calcite = 1E-2;
  previous 1000; %umol/l/year
Calcium = 1000;
  previous 10000; % calcium concentration [uM?]

## Slide 9: Bug and debug

## Slide 10: Different Scenarios under Coupled Model - Methane Hotspot
T=30;
  degree C;Summer
O2init=50;
  uM; Anoxic
SO4init = 200;
  uM; Freshwater
NPP = 800;
  g/m2/yr; High OC
Vbottom=1;
  cm/yr; Backwater

## Slide 11: Different Scenarios under Coupled Model - Spring Mountainous
T=5;
  Early Spring
O2init=350;
  uM; Oxic
SO4init = 500;
  uM; Medium
NPP = 10;
  g/m2/yr; Low OC
Vbottom=100;
  cm/yr; Turbulent

## Slide 12: Different Scenarios under Coupled Model - Carbonate Burial
O2init=200;
  uM; Normal
SO4init = 3000;
  uM; High
DICinit=3000;
  uM; High IC
HCO3init = 2000;
  uM; High ALK
NPP = 150;
  g/m2/yr; Mid OC
Vbottom=10;
  cm/yr; Medium

## Slide 13: Next Step -Adding Input for USGS stations
Expecting Input
T
O2
ALK/DIC
POC conc
Grain Distribution
  for Porosity
Sheer V=gHS-2
  for POM setting rate and Hyporheic diffusion
SO4?; for CH4 proxy
Expecting Output
CH4 proxy
  Anoxic Depth/Rate_Meth
Carbonate Burial
  sigma_carb

## Slide 14: Estuary

## Slide 15: Freshwater